## Slide 1: MAX17320 schematic concern #1
Back-to-back mosfet is required in MAX17320. It should be in opposite orientation like following. The MOSFET circuit is a load switch application, and block the current is bidirectional

## Slide 2: MAX17320 schematic concern #2
I notice that your battery input is directly flowing to the battery pack. It does not go through MOSFET circuit. Therefore, it will not have the load switches feature between charger and battery.

## Slide 3: MAX17320 schematic concern #3
your CSP and CSN is not in use. Does not have the current sense resistor. It will affect and not able to perform the fuel gauge feature.

## Slide 4
MAX17320
LTC4162-L
Li-ion cell x2
24V
16V
Li-ion cell x2
Li-ion cell x2
Li-ion cell x2
New Proposal to power tree
MP2759
MPM3620
MPM3620
MAX42402
MAX42402
3.3V
5V

## Slide 5: MAX42402/MAX42403/MAX42405/ MAX42406/MAX42408/MAX42410
36 V Monolithic Buck Regulators, 2.5 A to 10 A
https://www.analog.com/media/en/technical-documentation/data-sheets/max42402-max42403.pdf
https://www.analog.com/media/en/technical-documentation/data-sheets/max42405-max42406.pdf
https://www.analog.com/media/en/technical-documentation/data-sheets/max42408-max42410.pdf

## Slide 6: MAX4240x to MAX42410: Value Proposition and Key Benefits
Value Proposition
Low noise, symmetrical VIN pinouts
High efficiency
Low quiescent current
Key Benefits
Low EMI solution for applications that require superior EMI performance
Lower loss and better thermal performance at all load ranges with skip mode operation
Portable devices require low power consumption even at standby for extended battery life
Typical Application Circuit
MAX42402
MAX42403
MAX42405
MAX42406
MAX42408
MAX42410
Block Diagram

## Slide 7: MAX4240x to MAX42410: Product Positioning
Features and Specifications
High efficiency and low IQ
Low noise, spread spectrum for low EMI
MIN on time
ADI Portfolio Positioning
Very cost-competitive with high efficiency and low IQ in ADI buck offerings
Very cost-competitive in the silent switcher family of LT parts
Lowest MIN on time
Notes: This slide shows proof of this product’s strengths.